## Slide 1: Bpftime: Userspace eBPF runtime
https://github.com/eunomia-bpf/bpftime
Yusheng Zheng
yunwei356@gmail.com

## Slide 2: Bpftime: Userspace eBPF runtime
bpftime, a full-featured, high-performance eBPF runtime designed to operate in userspace：
Fast Uprobe and Syscall hook capabilities
Userspace uprobe can be 10x faster than kernel uprobe
  Trace the functions or modify the function calls
Programmatically hook all syscalls of a process safely and efficiently.
  Monitor or Modify the syscall behavior
Compare to:
  Wasm in userspace
  eBPF in kernel space
  Other userspace eBPF runtime and toolchains
  Other plugin systems or runtimes

## Slide 3: Motivation
1. Kernel Uprobe Performance Issues
Current UProbe implementation necessitates two kernel context copies.
Results in significant performance overhead.
Not suitable for real-time monitoring in latency-sensitive applications.
Uprobe's Wide Adoption in Production
Traces user-space protocols: SSL, TLS, HTTP2.
Monitors memory allocation and detects leaks.
Tracks threads and goroutine dynamics.
Provides passive, non-instrumental tracing.
And more...

## Slide 4: Motivation
2. Kernel eBPF Security Concerns and limited configurable
eBPF programs run in kernel mode, requiring root access.
Increases attack surface, posing risks like container escape.
Inherent vulnerabilities in eBPF can lead to Kernel Exploits.
Verifier has limited the operation of eBPF, config requires kernel change

## Slide 5: Motivation
3. Wasm Runtime or other plugin systems Limitations
Manual integration needed, making it less adaptable to API version changes.
Relies on underlying libraries for complex operations, e.g., Wasi-nn.
Security concerns with external APIs like Wasi require additional validation and runtime checks, leading to high performance costs.
eBPF: performance first and security second, use verifier for security
Wasm: puts more emphasis on security at the cost of some runtime overheads, use SFI for security

## Slide 6: Current eBPF userspace Runtimes
Ubpf: ELF parsing, simple hash map, arm64, x86 JIT.
Rbpf: Helper mechanism, x86 JIT, VM. GitHub.
Drawbacks:
  Complex integration and usage, cannot use kernel eBPF library and toolchains, e.g. libbpf/bpftrace/clang
  No attach support. No interprocess maps.
  Limited functionality in userspace.
  JIT supports for only arm64 or x86

## Slide 7: Existing Non-linux eBPF Usecases
Qemu+uBPF: Combines Qemu with uBPF. Video.
Oko: Extends Open vSwitch-DPDK with BPF. Enhances tools for better integration. GitHub.
Solana: Userspace eBPF for High-performance Smart Contract. GitHub.
DPDK eBPF: Libraries for fast packet processing. Enhanced by Userspace eBPF.
eBPF for Windows: Brings eBPF toolchains and runtime to Windows kernel.
Papers:
Rapidpatch: Firmware Hotpatching for Real-Time Embedded Devices
Femto-Containers: Lightweight Virtualization and Fault Isolation For Small Software Functions on Low-Power IoT Microcontrollers
Networks + plugins + edge runtime + smart contract + hotpatch + Windows

## Slide 8: Features of bpftime
Run eBPF in userspace just like in the kernel
Achieve 10x speedup vs. kernel uprobes.
Use shared eBPF maps for data & control.
Compatible with clang, libbpf, and existing eBPF toolchains; supports CO-RE & BTF.
Support external functions(ffi) and pointers
Includes cross-platform interpreter & fast LLVM JIT compiler & handcraft x86 JIT in C for limited resources, Near to native speed
Inject eBPF runtime to Any running Process without restart or manually recompile
Runing not only in Linux: all unix system and windows, even Iot devices

## Slide 9: Examples
Use uprobe to monitor userspace malloc function in libc, with hash maps

## Slide 10: Examples
Use syscall tracepoint to monitor open and close syscall, with ring buffer for output

## Slide 11
eBPF program
eBPF program source
Existing eBPF toolchains：clang/bpftool/bpftrace…
eBPF userspace applications
eBPF bytecode
eBPF maps
bpf syscall
verifier
JIT compiler
Target process
Uprobe
Trap
breakpoint
tracepoint
syscall
kprobe
socket
load
attach
Userspace library: libbpf…
load
Userspace
Userspace
Kernel space
attach
Original Kernel eBPF
function
Context switch

## Slide 12
eBPF program source
Existing eBPF toolchains：clang/bpftool/bpftrace…
eBPF userspace applications
eBPF bytecode
bpf function call
Target process
Share memory
inlineHook
tracepoint
uprobe
socket
attach
Userspace library: libbpf…
Userspace
inject
bpftime: userspace eBPF
function
eBPF maps
bpftime-syscall.so
verifier
bpftime-agent.so
program
JIT AOT compiler
kprobe
syscall
bpf syscall
load
Kernel space

## Slide 13: Benchmark

## Slide 14: Benchmark
Exec time: Left to right: ubpf jit, rbpf jit, llvm jit/aot, wasm, native
LLVM jit can be the fastest
LLVM is heavy? AOT is on the way

## Slide 15: More is coming…
Figure out how to run it together transparently with kernel probe
An AOT compiler for eBPF can be easily added based on the LLVM IR.
More examples and usecases.
…
This project is open-sourced by https://github.com/eunomia-bpf/bpftime

## Slide 16: bpf-developer-tutorial
https://github.com/eunomia-bpf/bpf-developer-tutorial
1.1k+ stars in Github
10W+ readings on various Platform: zhihu, wechat, juejin…

## Slide 17: AI for eBPF code Generation
https://gpt-2-bpftrace.vercel.app/
https://github.com/eunomia-bpf/GPTtrace
KEN project （Not yet open-sourced）
GPT4 can generate eBPF code up to 80% correct with our AI agents